## Slide 1: YAPT Automate provisioning devices
Christian Klewar (cklewar@juniper.net)
Version 0.3 / September 2017
Yet Another Provisioning Tool – Phone Home

## Slide 2: YAPT Use Cases
Zero Touch provisioning
Provisioning
Verify configuration / connectivity after provisioning
Verification
Automate replacement of device in case of failure
RMA

## Slide 3: YAPT Provisioning Scenarios
Staging Area
Drop shipping
Ship device directly to final destination
Devices being provisioned on site
Use staging area / network to provision devices
Ship / place devices after provisioning is done

## Slide 4: Phone Home

## Slide 5: Automated Secure Provisioning (ASP) Based upon the YAPT server by Christian Klewar
Device Config Repository
Space & SD / etc
Upon initial boot-up, Device’s Phone-Home contacts redirect.juniper.net
redirect.juniper.net passes the address of customer configuration server to the Device
Device handshakes with configuration server and obtains its specific config
ASP instantiates management platform
ASP in place for RMAs, upgrades
Enterprise Remote Branch / Campus
1
2
3
4
SRX / NFX
redirect.juniper.net
ASP Config Server
Enterprise DC / Cloud
Food
Internet
0
0.1
Device configurations are generated
Authentication for installations

## Slide 6: Methods and Features
YAPT (ASP) is unique as a provisioning solution, addressing the following feature requirements for wide-area remote-branch deployments
    Phone-Home Server to respond as the Config Server to request redirected from the Juniper Phone Home Redirect service; YAPT can implement the Activation Code to ensure the Device requesting config is where it should be, in the right hands
    Outbound SSH (OSSH) support for case where Device calls into the Config Server (esp. behind NAT where response from Config Server fails and does not reach the Device)
    X.509 Certificate Support for PKI-based IPsec tunneling in the Branch device: Secure pass-through of X.509 Cert from CA
YAPT can also serve as Bench or Campus server for initial provisioning
    Can serve as the solution to expedite staged and field deployments locally
    Supports DHCP, TFTP and REST, as well as OSSH and SRX/NFX Phone-Home
YAPT is Extensible, leveraging RabbitMQ Message Bus and Plug-In Service Module -based architecture
    New modules can easily be added to extend services / features

## Slide 7: PS Service: Jumpstart base solution for Engagement Basic Deployment & Support: Insertion for Value-Add Services
Open-Source – Free basic solution
Freemium: (Jumpstart) Add Support and Ease of Operation
    Cloud-served (hosted option),
    Supported (JTAC / PS)
Premium/Ultimate: (Engagement Upsell) Value-Added Enterprise Services
    Develop configuration and initial build & test
    Automated Tailored Test Environment – ongoing validation
    Process Integration – connection to business processes and IT tools (i.e. J-EDI)
Juniper Services Engagement for Customer Intimacy (Stickiness)
Premium
Freemium
Free
Ultimate

## Slide 8: Phone Home Capabilities (PHS / PHC)
Branch A
Order branch device and drop ship it to final destination
Obtain device serial number to activate provisioning device by:
  Smartphone App which uses GPS location data / barcode reader
  User phone call / email to providing serial number to central IT
Automatically call redirect.juniper.net
Using phone home client
Provisioning server site A
Provisioning server site B
Juniper redirect service portal
Branch A -> redirect to server site A
Branch B -> redirect to server site B
Branch X -> redirect o to server site X
Response: you are branch A go to provisioning server site A
Branch A device connects to provisioning server at site A
Device A authenticates and provision process is being started

## Slide 9: YAPT - Architecture
Backend
Services
Source Plugins
Message Broker / Bus
Task Plugins
Internal
SQL
Webserver
Software
Configuration
IPAM
Space
UI Connector
Bus Connector
Bus Connector
Graphical Interface
Bus Connector
…
OSSH
TFTP
DHCP
Bus Connector
Broker Messages
SSH
REST
FILE
Internal Messages
QFX/EX/NFX
SRX
SSH / Netconf
Trigger Event

## Slide 10: Services / Source Plugins (PHS)
PHS service listening for inbound http/s connections
PHS service authenticates device / detect device type
Source plugin “phs” normalizes received data and sends to Message Broker
Backend
Message Broker / Bus
Task Plugins
Webserver
Software
Configuration
IPAM
Space
Bus Connector
Graphical Interface
Bus Connector
Backend
Internal
SQL
UI Connector
Bus Connector
…
Service
Source Plugin
OSSH
TFTP
DHCP
Bus Connector
Services
SSH
REST
FILE
SRX
Services
Source Plugins
Message Broker / Bus
PHS
Bus Connector
HTTP/S
http/https connection
Task Plugins
New device
Configuration
IPAM
Cert
Bus Connector
New device
Port Forward
CA Server
Netconf commit config
REST
IPAM Server
§
Send certs request

## Slide 11: Services / Source Plugins (OSSH)
OSSH service listening for inbound ssh connections
OSSH service authenticates device
Source plugin “ossh” normalizes received data and sends to Message Broker
Backend
Message Broker / Bus
Task Plugins
Webserver
Software
Configuration
IPAM
Space
Bus Connector
Graphical Interface
Bus Connector
Backend
Internal
SQL
UI Connector
Bus Connector
…
Service
Source Plugin
OSSH
TFTP
DHCP
Bus Connector
Services
SSH
REST
FILE
SRX
Services
Source Plugins
Message Broker / Bus
OSSH
Bus Connector
SSH
Outbound-ssh connection
Task Plugins
New device
Configuration
IPAM
Cert
Bus Connector
New device
Port Forward
CA Server
Netconf commit config
REST
IPAM Server
§
Send certs request

## Slide 12: Thank You